## Slide 1: Solutions Engineer Interview Exercise
David J. Levine
Solutions Engineer Candidate

## Slide 2: Overview of the Project
Task 1: Vision
  Configure a basic camera component and use Viam’s vision service to implement a simple object detector
Task 2: Cloud Integration
  Configure Viam’s data capture service to store camera frames into the cloud
  How could we use this data to possibly create a custom model?
Task 3: Modular Registry
  Create a custom sensor (calling the previously created vision service)
  Should have a single field called “person detected”
  Set to 1 if a person is detected, and 0 if no person is detected

## Slide 3: Platform architecture
App.viam.com
Cloud storage
Smart machine part:
david-macbook-main
CLOUD
viam-server
Webcam:
(“cam“)
ML Model
”people”
EfficientDet-COCO
Vision Service:
“myPeopleDetector”
Calls “people”
Manages machine config, API access for SDK scripts
Python SDK Scripts (runs locally)
Custom sensor-1 component:
Uses custom module “sensor-pd“
Custom software module:
“sensor-pd“
Notes: The diagram shows how my local Python SDK script communicates with the Viam Cloud using an API key, which then routes to the local viam-server
The camera feed is processed through the EfficientDet ML model (people)
The Vision service (myPeopleDetector) wraps this and provides a simple detection interface
All components are configured via the Viam UI, no manual JSON was needed for setup
The JSON configuration reflects this architecture and was auto-generated by the platform
“The local component sensor-1 is an instance of the model dl-org:sensor-pd:pdetect, which is defined in my custom module sensor-pd.”
Here’s how that breaks down:
Module: sensor-pd – This is the local Python module you developed.
Model: dl-org:sensor-pd:pdetect – The unique identifier for the person detection sensor logic.
Component: sensor-1 – The actual, running instance of the sensor on your local Viam machine.

## Slide 4: Overview of the Project Directory
From GitHub README: https://github.com/djlev8/viam-interview-project/tree/main
From Viam dashboard

## Slide 5: Task 1: Vision Service and Object Detection
Goal: Set up a webcam → ML model (EfficientDet-COCO) → Vision Service → SDK-based person detection
Configured webcam test
Configured webcam JSON
Following the ‘Detect a Person and Send a Photo’ tutorial.
Notes: I first created a new machine called david-macbook-main, and then configured a webcam component
I used a discovery service to find the correct video_path for my built-in camera, since it did not come up automatically
Here you see the configured camera, showing its view of me once a second.

## Slide 6: Task 1: Vision Service and Object Detection
Goal: Set up a webcam → ML model (EfficientDet-COCO) → Vision Service → SDK-based person detection
EfficientDet-COCO model deployed
Vision Service created and linked to model
Detection UI
Notes: The camera feed is processed through the EfficientDet ML-COCO model (people) from viam-labs
The Vision service (myPeopleDetector) wraps this and provides a simple detection interface
All components are configured via the Viam UI, no manual JSON was needed for setup
The JSON configuration reflects this architecture and was auto-generated by the platform

## Slide 7: Task 1: Vision Service and Object Detection
Goal: Set up a webcam → ML model (EfficientDet-COCO) → Vision Service → SDK-based person detection
Terminal Output: Person Detected
Code snippet from detection script (vision_service.py)
Used SDK to filter for confident (> 0.5) ‘Person’ detections, instead of printing all detections found, regardless of class name or confidence
Notes: 🔍 What I Did in the Script:
Connected to my smart machine using RobotClient and a secure API key:
Even though the script runs locally, it connects via the cloud to route securely to my local viam-server.
This mirrors how customers would interact with remote robots.
Loaded key Viam components:
Camera: Accessed live video feed from my MacBook’s webcam (cam)
MLModel: Loaded metadata about the deployed EfficientDet-COCO model (people)
Vision Service: Used myPeopleDetector to interpret results from the model
Filtered detections using the SDK:
Called get_detections_from_camera("cam")
Applied logic to only keep detections where:
confidence > 0.5
class_name == "Person" (case-sensitive match to model output)
Printed filtered detections to verify successful pipeline from:
Camera → ML Model → Vision Service → SDK
Closed the robot client to clean up the connection properly.

## Slide 8: Task 1: Vision Service and Object Detection
Challenges & Debugging:
Encountered webcam connection error
  Restarted viam-server and reconnected successfully
  CLI: viam-server -config ~/Downloads/viam-david-macbook-main.json
Needed to use discovery service to retrieve valid video path for my built-in webcam
Filtered through list of detections to find confident ‘person’ only detections after first obtaining all detections
Webcam connect error
Initial output: Detecting many objects
Notes: Original code:
detected_people = await people_detector.get_detections_from_camera("cam")
print("peopleDetetctor get_detections_from_camera return value: {detected_people}")
Changed to: detected_people = [
person for person in (await my_people_detector.get_detections_from_camera("cam"))
if person.confidence > 0.5 and person.class_name == "Person"
]
print(f"detected_people: {detected_people}")

## Slide 9: Task 2: Data Capture & Cloud Storage
Data management service enabled
Data capture settings specified (capture rate = 1 Hz, MIME type = JPG)
Note: Needed to create data management service prior to configuring data capture with configured camera.
Goal: Create data-manager service → Set capture rate & ReadImage method → Store frames to cloud
Following the ‘Capture and sync edge data’ document.

## Slide 10: Task 2: Data Capture & Cloud Storage
Goal: Create data-manager service → Set capture rate & ReadImage method → Store frames to cloud
Images stored to the cloud
Installed viam CLI to run image export
viam data export --robot-id <robot-id> --component-name cam --method ReadImage --output ./exported_data

## Slide 11: Task 2: Data Capture & Cloud Storage
Images stored to the cloud with detection details from myPeopleDetector Vision service
Goal: Create data-manager service → Set capture rate & ReadImage method → Store frames to cloud

## Slide 12: Task 2: Discussion – How the data enables custom models
I enabled cloud logging for the cam component, which allowed me to capture image frames from my MacBook’s webcam directly to the Viam cloud.
This type of captured image data is valuable for:
  Evaluating model accuracy: comparing what the model detects vs what’s actually in the frame.
  Labeling custom datasets: using stored images and metadata to label people or other objects.
  Retraining or fine-tuning models: creating a customer-specific version of EfficientDet-COCO that performs better on their environment or edge cases.
Exported image data and detection logs can be used to train or validate models in frameworks like PyTorch, TensorFlow, or AutoML pipelines.
Going forward, combining image data with detection metadata (e.g., bounding boxes + class + confidence) provides a complete training set for a custom object detector.
Notes: Steps to do this programmatically: 1. Connect to the Robot
Use the Viam Python SDK to authenticate and connect.
from viam.robot.client import RobotClient
async def connect():
return await RobotClient.at_address(
'your-machine-name.viam.cloud',
RobotClient.Options.with_api_key(
api_key='your-api-key',
api_key_id='your-api-key-id'
)
)
2. Access the Camera
Use the SDK to access the configured camera component:
from viam.components.camera import Camera
camera = Camera.from_robot(robot, 'cam')
3. Capture an Image
Capture an image frame from the camera:
image = await camera.get_image()
4. Use the Data Capture Service
Call the capture_image method to store it in the Viam cloud:
from viam.services.datacapture import DataCaptureClient
data_capture = DataCaptureClient.from_robot(robot)
await data_capture.capture_image(camera_name='cam')

## Slide 13: Task 3: Modular Registry: Overview
Goal: Build a custom sensor module that uses the Vision service I previously created and returns:
{’person_detected’: 1} if a person is visible to the camera,
and
{’person_detected’: 0} if a person is NOT visible to the camera.
Steps:
1) Module Setup
2) Implementation of the Component API
3) Adding the Custom Sensor Component to my Machine
4) Local Testing
5) Error Handling & Fixes
Following the ‘Integrate other physical or virtual hardware’ document.

## Slide 14: Task 3: Modular Registry: Module Setup
Goal: Scaffold and generate the custom module, generating the necessary stub files (in the sensor-pd folder).
From the CLI, I used viam module generate and followed the relevant prompts.
Module successfully generated!
Prompts filled:
Name: sensor-pd
Language: Python
Visibility: Private
Namespace/Org-ID: dl-org
Resource to be added: Sensor Component
Model name: pdetect
Cloud build? Yes
Register module? Yes
Notes: Terminal command used to scaffold a new custom Viam sensor module named `sensor-pd`, specifying Python as the language, setting it as private, and registering it under the `dl-org` namespace.
Confirmation message from the Viam CLI showing successful creation of the module folder structure and initialization of boilerplate code.

## Slide 15: Task 3: Modular Registry: Module Setup
Goal: Scaffold and generate the custom module, generating the necessary stub files (in the sensor-pd folder).
Final file structure within the generated sensor-pd folder:
I added or changed files from the auto-generated structure to implement my custom sensor logic and enable local development and testing:
reload.sh (I added)
  Script I wrote for hot reloading the module locally.
meta.json (I modified)
src/models/pdetect.py (I modified)
src/main.py (I modified)
Notes: sensor-pd/
🔹
build.sh
Used for cloud builds (optional).
A shell script used to automate the packaging of your module into a .tar.gz file. While optional in local development, it’s useful if you later want to deploy your module via cloud builds on Viam.
🔹
meta.json
Module manifest file.
Describes your module to Viam. It contains:
entrypoint: The script to run the module (e.g., reload.sh).
build: Instructions for packaging and building your module.
model: The namespace triplet (dl-org:sensor-pd:pdetect) that describes the model your component implements.
arch: Architectures the module supports (linux/amd64, etc.).
🔹
module.tar.gz
Packaged version of your module.
Automatically created during build. This archive contains all code, configs, and scripts needed for your module to run on the Viam RDK.
🔹
reload.sh
Hot-reload entrypoint for local development.
Executes setup and then launches main.py. Used during viam module reload --local to allow rapid iteration without cloud build.
🔹
requirements.txt
Python dependencies.
Specifies the Python packages required to run the module, including viam-sdk. Installed during setup via setup.sh.
🔹
run.sh
Optional script for local testing.
Often used as a convenience script to run the module without Viam’s tooling. You may use this to simulate startup locally outside of the Viam UI.
🔹
setup.sh
Sets up a virtual environment.
Creates a .venv, installs dependencies from requirements.txt, and prepares your environment for development and testing.
sensor-pd/src/
🔹
main.py
Module startup script.
Registers your custom model (dl-org:sensor-pd:pdetect) and launches the module. This is where your resource is added to Viam’s registry and your component gets connected to the machine.
sensor-pd/src/models/
🔹
pdetect.py
Your custom sensor implementation.
Defines the Pdetect class, a sensor that wraps a Vision service to detect people in a camera feed. It includes:
validate_config(): Checks that the camera name and dependencies are set.
reconfigure(): Dynamically updates the component config.
do_command(): Calls the Vision service to check for people.
get_readings(): Wraps do_command() and exposes a binary result.

## Slide 16: Module Architecture: How main.py Registers and Runs the Custom Sensor
main.py is launched by reload.sh.
  It loads the module via Module.from_args().
  Registers my sensor model (dl-org:sensor-pd:pdetect) into Viam’s resource registry.
The model points to the Pdetect class in pdetect.py.
  When a resource is created (e.g., sensor-1 in the Viam UI), Viam uses the model triplet to instantiate this model.
pdetect.py:
  Queries the Vision Service (like myPeopleDetector) to detect people via camera feed.
  Returns person_detected = 1 or 0.
The Viam App shows live logs and values via the UI, helping me debug and monitor sensor results.

## Slide 17: Task 3: Modular Registry: Module Implementation
Goal: Add custom logic to Pdetect class (pdetect.py) to execute the goals of Task 3. Following the docs & looking at the ‘simple-module’ example in the Viam Python SDK, I had to make sure I edited the following within Pdetect:
new()
validate_config()
reconfigure()
get_readings()
do_command()
Notes: Edit the validate_config function to do the following:
Check that the user has configured required attributes and return errors if they are missing.
Return a map of any dependencies.

## Slide 18: Task 3: Modular Registry: Implement the Component API
new():
This method is responsible for creating and returning a new instance of the Pdetect sensor class.
  It receives the config and dependencies from the Viam system.
  It initializes the sensor (sensor = cls(config.name)) and then immediately calls reconfigure() to apply the configuration and wire up dependencies.
  It returns the fully ready-to-use sensor instance.
Notes: The new() method is a class method used to instantiate the custom sensor when the module is initialized by Viam. It reates a new instance of the Pdetect class using the name from the component’s configuration.
Calls reconfigure() to initialize any attributes and dependencies based on the current config.
Returns the fully constructed and configured sensor instance.

## Slide 19: Task 3: Modular Registry: Implement the Component API
reconfigure():
Triggered when the component’s configuration is updated in the Viam app
  Reads the latest camera_name and detector_name value from the incoming config
  Retrieves the required dependency detector_name from the dependency map (throws error if not available)
  Casts the required dependency as the correct type
  Stores vision client and camera name internally as instance variables for use in detection logic in do_command()
  Prepares the module for dynamic behavior based on configurable dependency names
Notes: INSTANCE METHOD
Ensures that the user has provided a camera_name attribute in the JSON config.
If not, it throws a helpful error early.
Takes the configured camera name (e.g., "cam") and stores it in an instance variable.
This value will later be used to query the correct camera when detecting people.
Looks up the required myPeopleDetector Vision service from the dependencies dictionary.
Throws a clear error if it’s not available.
Stores the vision client as self.vision so it can be used later in do_command() and get_readings().
Calls the parent class’s reconfigure() method to handle any internal SDK logic.

## Slide 20: Task 3: Modular Registry: Implement the Component API
validate_config():
Ensures that the user-supplied configuration is valid before the module is started.
  Checks for required attributes: camera_name (required attribute) and detector_name (required attribute & dependency)
  Raises errors if required fields are missing or improperly typed
Declares required and optional dependencies for the module.
  Dependencies returned: required: detector_name
  This tells Viam to pass in the Vision service resource with this name at runtime.
Note:
camera_name is a required attribute because it’s just a string used to route the vision query to the correct camera.
detector_name is a required dependency, since our module needs access to the actual Vision service object to perform detection.
Notes: Edit the validate_config function to do the following:
Check that the user has configured required attributes and return errors if they are missing.
Return a map of any dependencies.
Prevents runtime failures by enforcing configuration rules up front.
  Allows Viam to wire up resource dependencies automatically (like linking to a vision service).

## Slide 21: Task 3: Modular Registry: Implement the Component API
do_command():
Allows the sensor to query the `myPeopleDetector` vision service and returns `person_detected: 1` if a person is seen with >0.5 confidence, otherwise 0.
Notes: The do_command() method implements the core logic for person detection. It is triggered when a custom command is issued to the sensor component.
Specifically, it: Uses the injected VisionClient (myPeopleDetector) to query the camera (specified via camera_name) for detected objects.
Iterates through the detections and checks for any objects with the class "person" and confidence > 0.5.
Returns a simple dictionary result: { "person_detected": 1 } if a person is found.
{ "person_detected": 0 } if no person is detected.
This method powers both real-time detections and supports Viam’s get_readings() sensor API through internal calls.

## Slide 22: Task 3: Modular Registry: Implement the Component API
get_readings():
  sensor interface that Viam calls to retrieve the latest data from the sensor.
  Invokes the internal do_command method to perform the actual person detection logic.
Wraps the result from do_command in a dictionary with a consistent sensor reading key:
  Returns: {"person_detected": 1} if a person is detected, Returns: {"person_detected": 0} if no person is detected.
This method ensures compatibility with the Viam Sensor API, allowing the module to be used like any other built-in Viam sensor.
Notes: The get_readings() method is the public-facing sensor interface that Viam calls to retrieve the latest data from the sensor. Specifically, it: Invokes the internal do_command() method to perform the actual person detection logic.
Wraps the result from do_command() in a dictionary with a consistent sensor reading key: Returns: { "person_detected": 1 } if a person is detected.
Returns: { "person_detected": 0 } if no person is detected.
This method ensures compatibility with the Viam Sensor API, allowing the module to be used like any other built-in Viam sensor.

## Slide 23: Task 3: Modular Registry: Implement the Component API
main.py:
  Uses Viam’s registry to register the pdetect model under the Sensor API, linking the model name (dl-org:sensor-pd:pdetect) to my Pdetect implementation.
  Includes error handling to avoid duplicate registration when hot reloading.
  Attaches the registered model to the module so it can be discovered and used by Viam.
  Initializes and launches the module to connect with the Viam cloud, enabling remote control and configuration.
Notes: The main.py script is the entry point for the sensor-pd module.
It performs three core functions:
Registers the custom model: Uses Viam’s registry to register the pdetect model under the Sensor API, linking the model name (dl-org:sensor-pd:pdetect) to your Pdetect implementation. Includes error handling to avoid duplicate registration when hot reloading.
Adds the model to the module: Attaches the registered model to the module so it can be discovered and used by the Viam RDK.
Starts the module runtime: Initializes and launches the module to connect with the Viam cloud, enabling remote control and configuration.

## Slide 24: Task 3: Modular Registry: Local Testing
Goal: Test my custom module locally.
Steps to configure my local module on my machine
Notes: 🛠️ Prepare to Run Your Module (Local Dev Setup)
Create a reload.sh Script
This script ensures your module restarts properly during development.
It activates your Python virtual environment and runs main.py.
Make reload.sh Executable
chmod 755 reload.sh
Create Your Virtual Environment
Run the provided setup.sh script to create a .venv and install dependencies.
setup.sh
Update meta.json
Set "entrypoint" to "reload.sh"
Configure "build" to include setup.sh, your Python files, and supported platforms like "darwin/arm64"
This tells Viam how to package and run your module. 🧩 Configure Your Local Module on a Machine
Push Your Module to Viam
Run the hot reload command:
viam module reload --local --part-id <YOUR_PART_ID>

## Slide 25: Task 3: Modular Registry: Adding & Testing the Sensor Component
Goal: Add my custom sensor component in the Viam UI.
Notes: Add the Module in the Viam App
Go to your machine in the Viam web UI.
Click Add Resource ➜ choose Local Module ➜ Local Component.
Enter the Model Triplet
Example: dl-org:sensor-pd:pdetect
Select the appropriate API type (like Sensor).
Set a Name for Your Component
Example: sensor-1
Configure Attributes
Provide any required attributes in JSON format.
Example:
“camera_name”: “cam”

## Slide 26: Task 3: Modular Registry: Adding & Testing the Sensor Component
Goal: Test my custom sensor component in the Viam UI.

## Slide 27: Task 3: Modular Registry: Error Handling
Goal: Find errors and fix bugs to complete Task 3.
Errors: DuplicateResourceError: Cannot add resource with duplicate name "rdk:component:sensor/dl-org:sensor-pd:pdetect” → caused registration error (below)
  Cause:
    The module attempted to register the same resource more than once during hot reloads.
  Fix (main.py):
    Wrapped the registration line in a try/except block to catch and suppress the DuplicateResourceError.
Registration error caused by duplicate registration
try/except block to catch and suppress the DuplicateResourceError
After fix:
Before fix:
Notes: To prevent a DuplicateResourceError when reloading the module locally, I added a try/except block around the model registration step:
This catches the error that occurs when the module is hot-reloaded and the pdetect model has already been registered. Without this block, the module would crash and fail to start, resulting in the message:
“API ‘rdk:component:sensor’ with model ‘dl-org:sensor-pd:pdetect’ not registered”
By gracefully handling the exception, the module can safely restart without trying to re-register an already existing resource, allowing seamless local development and testing.
Error Handling: Duplicate Resource Error
Issue: “API with model not registered” even though model was implemented.
Root cause: module crashed on reload due to duplicate registration.
Fix: Wrapped Registry.register_resource_creator in a try/except block.
Outcome: Prevented crashes, enabled consistent hot reload behavior.
Takeaway: Defensive coding around registration improves module stability and UX during development.

## Slide 28: Task 3: Modular Registry: Error Handling
Goal: Find errors and fix bugs to complete Task 3.
Error: TypeError - Cannot instantiate typing.Union
  Cause:
    Attempted to wrap a basic type (int) inside SensorReading, which isn’t necessary and led to incompatible typing. (SensorReading is a type alias)
  Fix (pdetect.py → get_readings() method):
    Removed the use of SensorReading()and returned a plain int instead.
Type Error found in sensor_1 log
Removed the use of SensorReading()
After fix:
Before fix:
return {"person_detected": SensorReading(int(result["person_detected"]))}
return {"person_detected": int(result["person_detected"])}
Notes: My thinking was:
Since get_readings() should return a dictionary of sensor values, I assumed that each value should be a SensorReading object.
I tried to wrap the result of my do_command() call with SensorReading(...), assuming it was the correct format for Viam’s sensor API. return {"person_detected": SensorReading(int(result["person_detected"]))}
This error meant:
I was calling SensorReading(...), but SensorReading was not a class or constructor, and not meant to be instantiated directly.
In the Viam Python SDK, SensorReading is a typing alias, often defined like this:
SensorReading = Mapping[str, ValueTypes]
ValueTypes = Union[str, float, bool, int, list, dict, None]
I initially misunderstood SensorReading as a class or constructor and tried to cast a value to it. But SensorReading is just a type alias for Mapping[str, ValueTypes], so the correct way to satisfy the return type was to return a plain dictionary in that shape.
You can’t instantiate Union like a class — so this line failed because I was doing:
SensorReading(1) # ❌ This is invalid Instead of trying to create a SensorReading object, I just returned a regular dictionary of key-value pairs using native types (int, str, etc.), like this:
return {"person_detected": int(result["person_detected"])} This worked perfectly because Viam expects get_readings() to return a dictionary with native types — not custom class wrappers. Viam’s SensorReading is not a class — it’s a type alias.
Type annotations in Python (like Mapping[str, int]) are for static checking, not runtime behavior.
You can’t instantiate typing aliases like Union, Mapping, or Tuple directly.
When in doubt, stick with standard Python types (int, str, float) unless you know the SDK needs something special.

## Slide 29: Next Steps: Upload Module to Viam Registry
1. Set your module to public or private visibility.
When running viam module generate, choose whether others can access the module.
2. Update meta.json.
Ensure the entrypoint, build, path, and supported arch values are set correctly.
This file tells Viam how to build, package, and run the module.
3. Package your module.
Run the build command (or use build.sh) to create a module.tar.gz file.
4. Login to Viam.
5. Register your module.
6. Upload your module.
Push the module to the registry.
7. Use the module in the cloud.

## Slide 30: Opportunities for Improvement
Customizable Configuration via Viam UI
  Support configurable confidence thresholds, detection classes, and different camera inputs.
Capture & Store Data with Viam
  Extend to support other ML models beyond people detection in the Vision service.
  Integrate with Viam’s Data Capture UI to view and download results.
Build a UI for Sensor Control
  Develop a lightweight frontend to:
    Display live detection results from get_readings.
    Visualize logs and sensor state.
Robust Error Handling
  Add better exception management, validation, and user-visible error messages.
Developer Experience & Docs
  Publish module to Viam Registry.
  Include links to my GitHub, Docs, and example meta.json in the Registry.